## Slide 1: Error Detection & Correction
Data can be corrupted during transmission.
For reliable transmission, errors must be detected and corrected.
Error detection and correction can be implemented at the data link layer or at the transport layer of the OSI model.
There are two types of errors:
  Single bit error
  Burst error

## Slide 2: Single bit error
The single bit error means only one bit get changed of the data unit from 0 to 1 or 1 to 0.
A single bit error can happen if we are sending a data using parallel transmission.
For example, if eight wires are used to send all of the eight bits of a byte at the same time and one of the wire is noisy, one bit can be corrupted in each byte.
In serial transmission, the chances for a single bit error to occur are very less.

## Slide 3: Single bit error

## Slide 4: Burst error

## Slide 5: Burst error
A burst error means that two or more bits in the data unit have changed.
Burst error most likely to happen in a serial transmission.
The duration of noise is normally longer than the duration of a bit, which means that when noise affects data, it affects a set of bits.
The number of bits affected depends on the data rate and duration of noise.

## Slide 6: Multiple bit error

## Slide 7: Error Detection
Method 1:
  The sender will send two set of data unit.
  The receiving device would then be able to do a bit-for-bit comparison between the two versions of the data.
  Any discepancy would indicate an error, and an appropriate correction mechanism could be set in place.
  This method would be completely accurate, but it is very slow.
  The transmission time will be double and more extra time is added for comparison of every bits.

## Slide 8: Error Detection
Method 2
  Instead of repeating the entire data stream, a shorter group of bits may be appended to the end of each data unit.
  This technique is called redundancy because the extra bits are redundant to the information.
  They are discarded as soon as the accuracy of the transmission has been determined.
  Once the data stream has generated, it passes through device that analyzes it and adds on an appropriate coded redundancy check.
  The data unit is now enlarged by several bits, travels over the link to the receiver.
  The receiver passes the checking criteria, the data portion of the data unit is accepted and the redundant bits are discarded.

## Slide 9: Redundancy

## Slide 10: Detection Methods

## Slide 11: Vertical Redundancy Check(VRC)
It is least expensive method of error detection and often called, parity check.
In this technique, a redundant bit, called a parity bit, is appended to every data unit so that the total number of 1s in the unit becomes even.
For example,
1100001  1100001 1
1101010  1101010 0

## Slide 12: Even Parity VRC Concept

## Slide 13: VRC
Performance
  VRC can detect all single bit error.
  It can also detect burst errors as long as the total number of bits changed is odd.
    For example, 1000111011
    If any three bits get changed then the resulting parity will be odd and error will be detected.
    If two bits get changed then, the resulting parity will be even and error will not be detected.

## Slide 14: Longitudinal redundancy check (LRC)
In LRC, a block of bits is divided into rows and a redundant row of bits is added to the whole block.
Instead of sending 32 bits , it organize them in a table made of four rows and eight columns.
Then calculate the parity bit for each column and create a new row of eight bits, which are the parity bits for the whole block.

## Slide 15: LRC
11100111 11011101 00111001 10101001
11100111 11011101 00111001 10101001
LRC
10101010
1110011 11011101 00111001 10101001 10101010
Original Data plus LRC

## Slide 16: LRC
Performance
  LRC increases the likelihood of detecting burst errors.
  If two bit pattern of errors are damaged and two bits exactly in the same positions in another data unit are also damaged, the LRC checker will not detect error.
  For example,
    11110000 and 11000011
    If the first and last bit in each of them are changed, making the data units read 01110001 and 01000010, the errors can not be detected by LRC.

## Slide 17: Error Correction

## Slide 18: Redundancy Bits
Number of Data Bits | Number of Redundancy Bits | Total Bits (m+r)
1 | 2 | 3
2 | 3 | 5
3 | 3 | 6
4 | 3 | 7
5 | 4 | 9
6 | 4 | 10
7 | 4 | 11

## Slide 19: Hamming Code
Hamming code can be applied to data units of any length and uses relationships between data and redundancy bits .
Redundancy Bits:
  R1: bits 1,3,5,7,9,11
  R2 : bits 2,3,6,7,10,11
  R3: bits 4,5,6,7
  R8: bits: 8,9,10,11

## Slide 20: Hamming Code

## Slide 21: Hamming Code

## Slide 22: Hamming Code

## Slide 23
Single-bit error
Figure 9-21
WCB/McGraw-Hill
 The McGraw-Hill Companies, Inc., 1998

## Slide 24: Hamming Code

## Slide 25: Ethernet
Ethernet is IEEE 802.3 standards.

## Slide 26: Ethernet
IEEE Number | Common Name | Physical Technology | Bandwidth
802.3 | 10base2 | Thin coaxial cable in a bus topology | 10 Mbps
802.3 | 10Base5 | Thick coaxial cable for the backbone from each PC | 10Mbps
802.3u | 100BaseT for Fast Ethernet | Unshielded twisted pair in a star topology | 100 Mbps
802.3z | Gigabit | Ethernet fiber optic for the backbone, coaxial cable for the taps to the hub, all in the star topology | 1000Mbps

## Slide 27: CSMA/CD
A LAN needs a mechanism to coordinate traffic, minimize the number of frames that are delivered successfully.
The access mechanism used in an Ethernet is called carrier sense multiple access with collision detection (CSMA/CD).